## Slide 1
A0 | A1 | D0 | D1
Mode | Octaves |  | 
A2 | A3 |  | On
Steps / Dist | Scale |  | 
A0 | A1 | D0 | D1
Steps / Dist | Scale |  | 
A2 | A3 |  | Flash
Octaves | Mode |  | 
A0 | A1 | D0 | D1
Steps / Dist | Octaves |  | 
A2 | A3 | Flash | 
Mode | Scale |  | 
A0 | A1 | D0 | D1
Steps / Dist | Mode |  | 
A2 | A3 | On | On
Octaves | Scale |  | 
A0 | A1 | D0 | D1
Octaves | Scale |  | 
A2 | A3 | On | 
Steps / Dist | Mode |  | 
A0 | A1 | Default | 
Mode | Scale | D0 | D1
A2 | A3 |  | 
Steps / Dist | Octaves |  | 
Outputs
DAC output gives the 1V/Oct output to send to your oscillator.
D0 triggers every time the entire arpeggio sequence starts again.
D1 triggers every time the arpeggio changes octave.
Control Mode
Control mode allows you to select which controls are assigned to which of the analog inputs, and therefore which controls you can use CV to control, and which are manual only.
To enter Control Mode, turn the A3 control all the way up.
Then use the A2 control to select the layout you want (all variations detailed below).
The status of the two LEDs shows which layout you have selected.
Once you’ve selected your layout, turn down control A3 to return to normal operation.
You can also enter this mode on the fly using CV to achieve some extensive variations, switching between modes using a CV source. The same CV source will then influence different parameters once control mode is exited (which again, you would do by changing the appropriate CV). Some pretty complex automation of this can be achieved using voltage controlled switches.
Mode | Description
Up | Lowest to highest note
Down | Highest to lowest note
Up/Down | Lowest to highest then back; doesn’t repeat highest and lowest notes
Root-Up | Bounce between lowest and each other note in the series
Ping-Pong | Alternate from lowest to highest, moving towards middle note until all are played
Random | Plays one note from each octave selected
Scale
Major Pentatonic
Minor Pentatonic
Blues
Augmented
Ionian
Aeolian
Lydian
Mixolydian
Dorian
Phrygian
Locrian
Chromatic
Steps / Distance | 
Changing this control increases the distance and steps ranges. Distance (between each note played) is spread across the whole control range, then for each distance setting, the number of steps to be played in each arpeggio sits within that sub-range; i.e. select the distance setting you want, then fine tune for the number of steps. | 
Distance range | 1 - 6
Steps range | 3 - 6
Octaves
This simply selects the number of repeats of the arpeggio (1 to 5), with each being transposed to the next octave up.
FlexArp for ardcore
rockwoofstone sept 2013